## Slide 1: Problem Statement
Forbidden
Targets
Vehicle
Danger zone
For vehicles, given
Initial states, target locations, forbidden locations
Scheduled times of arrival (STA)
Earliest start times (EST)
Determine, with guarantees
Minimum-time trajectories
Latest start times (LST)

## Slide 2: Problem Statement
Forbidden
Targets
Vehicle
Danger zone
For vehicles, given
Initial states, target locations, forbidden locations
Scheduled times of arrival (STA)
Earliest start times (EST)
Determine, with guarantees
Minimum-time trajectories
Latest departure times

## Slide 3: Solution via Basic Reachability Theory
target set
avoid set

## Slide 4: Solution via Basic Reachability Theory
target set
avoid set
Hamilton-Jacobi Equation
Reachable set
States leading to target and avoiding collisions
Optimal liveness controller

## Slide 5: Solution via Basic Reachability Theory
target set
avoid set
Hamilton-Jacobi Equation
Reachable set
States leading to target and avoiding collisions
Optimal liveness controller
Reachable set
Target set
Avoid set

## Slide 6: Solution via Basic Reachability Theory
target set
avoid set
Hamilton-Jacobi Equation
Reachable set
States leading to target and avoiding collisions
Optimal liveness controller
Reachable set
Target set
Avoid set
: 4 vehicles with
4 destinations
: collision avoidance

## Slide 7: Solution via Basic Reachability Theory
target set
avoid set
Hamilton-Jacobi Equation
Reachable set
States leading to target and avoiding collisions
Optimal liveness controller
Reachable set
Target set
Avoid set
years
Petabytes
: 4 vehicles with
4 destinations
: collision avoidance
Exponential Scaling of Complexity w.r.t. # of vehicles!!

## Slide 8: Approximate Solution
Joint optimal solution is intractable!
Sequential path planning
Assign vehicle priorities
Treat higher-priority vehicles as moving obstacles
Forbidden
Targets
Vehicle
Danger zone

## Slide 9: Approximate Solution
Joint optimal solution is intractable!
Sequential path planning
Assign vehicle priorities
Treat higher-priority vehicles as moving obstacles
Forbidden
Targets
Vehicle
Danger zone

## Slide 10: Approximate Solution
Optimal Path Planning in Presence of Moving Obstacles

## Slide 11: Approximate Solution
target set
avoid set
Hamilton-Jacobi Variational Inequality[1]
Reachable set
States leading to target and avoiding collisions
Optimal liveness controller
Reachable set
Target set
Avoid set
Optimal Path Planning in Presence of Moving Obstacles
[1] Fisac, Chen, Tomlin, Sastry, HSCC 2015

## Slide 12: Approximate Solution
target set
avoid set
Hamilton-Jacobi Variational Inequality[1]
Reachable set
States leading to target and avoiding collisions
Optimal liveness controller
Reachable set
Target set
Avoid set
Optimal Path Planning in Presence of Moving Obstacles
: 1 vehicle with
destination
: higher priority vehicles
Repeat for each vehicle
linear scaling!
[1] Fisac, Chen, Tomlin, Sastry, HSCC 2015

## Slide 13: Four-Vehicle Example
Dynamics:
Scheduled Times of Arrival